| Item | Quantity | Designation | Price/unit EUR | Total EUR |
| --- | --- | --- | --- | --- |
| 1 |  | Supplying and laying of: m² wall panels P___ Wall sandwich element consisting of an external and internal steel cover shell connected in a shear-resistant manner via a heat-insulating rigid polyurethane foam core (density of approx. 40kg/m³) Requirement: approved by building authorities and quality-monitored Construction material class: Euro class B-s2, d0 or B-s3, d0 (flame retardant) Element thickness: ___ mm Heat transmission coefficient (u-value) certified to EN 14509 with joint: _____ W/m²(K (see data sheet PU insulating panel P) Effective width: 1150 mm Joint: double tongue-and-groove joint, precisely milled for precise fit during production Interior/exterior finish: Outer face: galvanized sheet steel 0.6 mm, polyester paint finish 25 µm, RAL xxxx; lined Internal face: galvanized stainless steel 0.5 mm, DU paint finish 10–15 µm, RAL 9002; lined Static system: Multi-span beam Rib spacing: approx. x.00 m Element length: up to x.00 m Supply and install vertically against a customer-supplied steel/timber beam framework in accordance with building authority approval and specialist rules of the IFBS. The wall elements must be fastened to the base construction by an externally visible fastener using rustproof fastening materials featuring a screw-type technology approved by the building authorities. All required fitting cuts as well as sealing, connection and fastening materials must be included in the calculation. Model and type to be offered as described: ROMA P___ |  |  |
| 2 |  | VARIANT: Panels with 25/ 25 µm coating Supplying and laying of: m² wall panels P ___ Wall sandwich element consisting of an external and internal steel cover shell connected in a shear-resistant manner via a heat-insulating rigid polyurethane foam core (density of approx. 40kg/m³) Requirement: approved by building authorities and quality-monitored Construction material class: Euro class B-s2, d0 or B-s3, d0 (flame retardant) Element thickness: 120 mm Heat transmission coefficient (u-value) certified to EN 14509 with joint: _____ W/m²(K (see data sheet PU insulating panel P) Effective width: 1150 mm Joint: double tongue-and-groove joint, precisely milled for precise fit during production Interior/exterior finish: Outer face: galvanized sheet steel 0.6 mm, polyester paint finish 25 µm, RAL xxxx; lined Internal face: galvanized stainless steel 0.6 mm, polyester paint finish 25 - 15 µm, RAL 9002; lined Supply and install vertically against a customer-supplied steel/timber beam framework in accordance with building authority approval and specialist rules of the IFBS. The wall elements must be fastened to the base construction by an externally visible fastener using rustproof fastening materials featuring a screw-type technology approved by the building authorities. All required fitting cuts as well as sealing, connection and fastening materials must be included in the calculation. Model and type to be offered as described: ROMA P___ |  |  |
| 3 |  | m drip profile Supplying and installing galvanized coated sheet steel in panel color, including fastening materials, sealing tapes and trimming Sheet thickness: 0.75 mm Layout: approx. 290 mm Bends: 4 |  |  |
| 4 |  | m roof parapet cover, 2-part made of galvanized base profile, Sheet thickness: 1.0 mm Layout: approx. 202 mm Bends: 2 and roof parapet profile made of galvanized coated sheet steel in panel color, Sheet thickness: 0.75 mm Layout: approx. 430 mm Bends: 6 Supplying and installing, including fastening materials, sealing tapes and trimming |  |  |
| 5 |  | m outside corner profile Supplying and installing galvanized coated sheet steel in panel color, including fastening materials and trimming Sheet thickness: 0.6 mm Layout: approx. 240 mm Bends: 3 |  |  |
| 6 |  | m inside corner profile Supplying and installing galvanized coated sheet steel in panel color, including fastening materials and trimming Sheet thickness: 0.6 mm Layout: approx. 240 mm Bends: 3 |  |  |
| 7 |  | U enclosure profile for wall openings Supplying and installing galvanized coated sheet steel in panel color, including fastening materials and trimming Sheet thickness: 0.6 mm Layout: approx. 222 mm Bends: 4 |  |  |